## Slide 1: Lab 1 – Driving in Shapes
MIT Beaver Works Racecar Curriculum
https://matthewcalligaro.github.io/RacecarWebsite/

## Slide 2: Lab Objectives
Main objective: Program the car to respond to controller input and drive in predefined shapes
Learning objectives
Use the start-update paradigm to create a program which can run on the car
Use the drive module to move the car
Use the controller module to respond to input from the Xbox controller in real time

## Slide 3: Finished Car

## Slide 4: Car Modes – Default Drive
When you launch a RACECAR program, the car starts in default drive mode so you can easily drive around
Accelerate forward
Accelerate backward
Start user program
Steer
Print message

## Slide 5: Car Modes – User Program
You can then tell the car to execute your Python program, which consists of a start and update function
  Start: run once when you enter user program mode
  Update: run 60 times per second in user program mode
Button |  | Effect
Start |  | Enter user program mode
Back |  | Enter default drive mode
Start + Back |  | Exit the program

## Slide 6: Car Modes – Starter Code
For each lab, you will be provided with a Python skeleton consisting of a blank start and update function
You will complete each lab by filling the start and update function
You may wish to add additional helper functions and global variables
################################################################################
# Imports
################################################################################
import sys
sys.path.insert(0, '../../library')
from racecar_core import *
rospy.init_node('racecar')
################################################################################
# Global variables
################################################################################
rc = Racecar()
################################################################################
# Functions
################################################################################
def start():
"""
This function is run once every time the start button is pressed
"""
pass
def update():
"""
After start() is run, this function is run every frame until the back button
is pressed
"""
pass
################################################################################
# Do not modify any code beyond this point
################################################################################
if __name__ == "__main__":
rc.set_start_update(start, update)
rc.go()
Example starter code

## Slide 7: Lab Logistics
git clone/pull
ssh/scp
1. The RACECAR files live on GitHub

## Slide 8: Lab Logistics
git clone/pull
ssh/scp
1. The RACECAR files live on GitHub
2. Clone the RACECAR files to your computer

## Slide 9: Lab Logistics
git clone/pull
ssh/scp
1. The RACECAR files live on GitHub
3. Edit the starter code on your computer
2. Clone the RACECAR files to your computer

## Slide 10: Lab Logistics
git clone/pull
ssh/scp
1. The RACECAR files live on GitHub
3. Edit the starter code on your computer
4. Copy the files to you RACECAR
2. Clone the RACECAR files to your computer

## Slide 11: Lab Logistics
git clone/pull
ssh/scp
1. The RACECAR files live on GitHub
3. Edit the starter code on your computer
5. Run the program on the RACECAR
4. Copy the files to you RACECAR
2. Clone the RACECAR files to your computer

## Slide 12: Key Modules – Drive
The Drive module allows us to move the car by setting its speed and the angle of the front wheels
Public interface
  set_speed_angle(speed, angle)
  stop()

## Slide 13: Key Modules – Drive Example
This update function will cause the car to drive forward for 1 second, drive to the left for 1 second, and then stop
def update():
global counter
if counter < 1:
# Drive forward at full speed
rc.drive.set_speed_angle(1, 0)
elif counter < 2:
# Drive to the left at full speed
rc.drive.set_speed_angle(1, -0.5)
else:
rc.drive.stop()
counter += rc.get_delta_time()

## Slide 14: Key Modules – Controller
The Controller module allows us to detect input from the Xbox controller
Public interface
  is_down(Button)
  was_pressed(Button)
  was_released(Button)
  get_trigger(Trigger)
  get_joystick(Joystick)
Button.A
Button.X
Button.RB
Button.Y
Button.B
Joystick.Left
Button.LB
Trigger.Right
Joystick.Right
Trigger.Left

## Slide 15: Key Modules – Controller Example
This update function uses input from the controller to decide how to move and when to print a message to the command line
def update():
# Enter this if block if RB is currently pressed
if rc.controller.is_down(rc.controller.Button.RB):
# Read the value of the right trigger to determine speed
speed = rc.controller.get_trigger(rc.controller.Trigger.RIGHT)
rc.drive.set_speed_angle(speed, 0)
# Print a message every time B is pressed
if rc.controller.was_pressed(rc.controller.Button.B):
print("The B button was pressed")

## Slide 16
Good luck and have fun!
Let us know if you need any help during the lab