## Slide 1: Lab 2
Color Images
This lecture is part of the RACECAR-MN introductory robotics course. You can visit the course webpage at mitll-racecar-mn.readthedocs.io.

## Slide 2: Objectives
Main Objective: Identify objects in a color image based on color
Learning Objectives
Learn how to use Jupyter notebooks
Use OpenCV functions to build image processing functions
Understand and implement proportional control

## Slide 3: Lab 2 Demo

## Slide 4: Color Space
Color models map input values to colors
Color space is a range of colors a color model covers
BGR models use measurements of blue, green, red
BGR
HSV

## Slide 5
Hue: the base color
  Range: 0°- 180°
Saturation: inverse the amount of white
  Range: 0 - 255
Value: inverse the amount of black
  Range: 0 - 255
H: 90°
S: 194
V: 207
HSV

## Slide 6
OpenCV
Using a color threshold, we can make masks from images
BLACK out the part of the image you want to remain hidden
WHITE out the part of the image you want to be seen

## Slide 7
Color Masking
Combine the color image with the black and white mask to make a color mask

## Slide 8
Color Masking
Color masks can be made with any black and white image.
White mask
Black mask
Full color
No color

## Slide 9
Contour Drawing
With color masks, we can identify objects and create contour drawings

## Slide 10
Common Issues
What issues might we have with these images and how would we address them?
Group activity

## Slide 11
Bang-Bang Control
Bang-Bang control uses feedback from the environment to switch between two states. This method of control oscillates around the set point in the acceptable bounds.

## Slide 12
Proportional Control
Proportional control uses feedback from the environment to proportionally set output values. Input is linearly proportional to output
Output
Input

## Slide 13: Camera Module
Retrieves color and depth images from the camera
Public Interface
  get_color_image()
  get_width()
  get_height()
  get_depth_image() (we'll use this next time)
Notes: https://mitll-racecar.readthedocs.io/en/latest/camera.html

## Slide 14: Display Module
Displays data and images to the screen
  Simulation: Creates a window on your computer
  RACECAR: creates a window on the mini-monitor
Public Interface
  show_color_image()
  show_depth_image() (we'll use this later)
  show_lidar() (we'll use this later)
Notes: https://mitll-racecar.readthedocs.io/en/latest/display.html

## Slide 15: Example 1
image = rc.camera.get_color_image()
for r in range(0, rc.camera.get_height()):
for c in range(0, rc.camera.get_width()):
foo = (image[r][c][0] + image[r][c][1] + image[r][c][2]) // 3
image[r][c][0] = foo
image[r][c][1] = foo
image[r][c][2] = foo
rc.display.show_color_image(image)
Group activity

## Slide 16: Example 2
image = rc.camera.get_color_image()
foo = 0
bar = (0, 0)
for r in range(0, rc.camera.get_height()):
for c in range(0, rc.camera.get_width()):
if image[r][c][0] > foo:
foo = image[r][c][0]
bar = (r, c)
print(bar)
Group activity

## Slide 17: Lab 2 Objectives
Jupyter Notebook: Write helper functions which use masks/contouring to identify objects based on color
Lab 2A: Implement line following
Lab 2B: Cone parking

## Slide 18: racecar_utils Library
Helper functions to process inputs/outputs of racecar_core
You will write everything in racecar_utils during the Jupyter notebook activates throughout the course
Documentation
Implementation

## Slide 19
Jupyter Notebooks
Example: lab2.ipynb