## Slide 1: Lab 4
LIDAR
This lecture is part of the RACECAR-MN introductory robotics course. You can visit the course webpage at mitll-racecar-mn.readthedocs.io.

## Slide 2: Objectives
Main Objective: Use LIDAR to detect objects around the car in all directions
Learning Objectives
Compare the advantages of the depth camera and the LIDAR, and identify ideal situations for each sensor
Convert raw LIDAR data into meaningful information about the surrounding environment
Understand and implement rudimentary path planning

## Slide 3: Depth Camera
What are some limitations of depth cameras?
Group activity

## Slide 4: Depth Camera
What are some limitations of depth cameras?
  Can only see in front of the car
  Do not work in the dark/poor lighting
  Noise and missing data
Group activity

## Slide 5: Depth Camera
What are some limitations of depth cameras?
  Can only see in front of the car
  Do not work in the dark/poor lighting
  Noise and missing data
On the other hand, LIDAR:
  Provides 360-degree vision
  Works in all lighting environments
  Can provide a second source of truth
Group activity

## Slide 6: Depth Camera
Group activity
Depth camera field of view = 74 degrees

## Slide 7: LIDAR
LIDAR (light + radar): Calculate object distance by firing a laser and measuring the time it takes to return
  Like radar but with a smaller wavelength of light
Group activity
radar
LIDAR
RACECAR
LIDAR

## Slide 8: LIDAR
Animation created by Mike1024

## Slide 9: LIDAR Limitations
Accuracy varies based on material
Subject to noise and null values
Poor performance in snow
Group activity

## Slide 10: RACECAR-MN LIDAR
YDLIDAR X4 (2D)
  $100 (cheap for LIDAR)
  Max range: 10 m
  Between 6 to 12 hz
720 samples returned as an array of floats
  0th entry = directly in front of the car
  Ordered clockwise

## Slide 11: Lidar Module
Retrieves the LIDAR scan
Public interface
  get_samples()
  get_num_samples()
Notes: https://mitll-racecar.readthedocs.io/en/latest/camera.html

## Slide 12: Display Module
Displays data and images to the screen
  Simulation: Creates a window on your computer
  RACECAR: Creates a window on the mini-monitor
Public interface
  show_color_image()
  show_depth_image()
  show_lidar()
Notes: https://mitll-racecar.readthedocs.io/en/latest/display.html

## Slide 13: Examples
# Example 1
scan = rc.lidar.get_samples()
foo = scan[450]
# Example 2
scan = rc.lidar.get_samples()
scan = (scan - 0.01) % 100000
bar = np.argmin(scan) * 360 / rc.lidar.get_num_samples()
# Example 3
scan = rc.lidar.get_samples()
baz = [e for e in scan[170:191] if e > 0.0]
qux = sum(baz) / len(baz)
Group activity

## Slide 14: Examples
# Example 1
scan = rc.lidar.get_samples()
foo = scan[450]
# Example 2
scan = rc.lidar.get_samples()
scan = (scan - 0.01) % 100000
bar = np.argmin(scan) * 360 / rc.lidar.get_num_samples()
# Example 3
scan = rc.lidar.get_samples()
baz = [e for e in scan[170:191] if e > 0.0]
qux = sum(baz) / len(baz)
Group activity
when would this cause an error?

## Slide 15: Lab 5 Objectives
Jupyter Notebook: Write helper functions to measure average distance and find the closest point in a scan
Lab 5A: Safety stop (revisited)
Lab 5B: Wall following
Revisit Phase 1 challenge