## Slide 1: Lab 4
IMU
This lecture is part of the RACECAR-MN introductory robotics course. You can visit the course webpage at mitll-racecar-mn.readthedocs.io.

## Slide 2: Objectives
Main Objective: Use the RACECAR’s IMU data to prevent rolling
Learning Objectives
Use the Physics module to retrieve linear acceleration and angular velocity

## Slide 3: Roll Prevention
Vehicle rollover is a threat for cars and trucks
  Turning too quickly can cause a vehicle with a high center of mass to roll

## Slide 4: Roll Prevention
It is difficult to roll the RACECAR-MN due to its low center of mass, but we will model this problem by artificially raising the center of mass in RacecarSim

## Slide 5
Rolling is caused by inertia
  When a car turns the inertial force continues linearly, which creates an outward force
There are various ways to prevent rolling:
Rolling Prevention
Super elevation
Wider turning
Reducing speed

## Slide 6
Internal Measurement Unit (IMU)
Uses accelerometers and gyroscopes to measure:
  Linear acceleration (acceleration data)
  Angular velocity (gyro data)

## Slide 7
Internal Measurement Unit (IMU)
Pitch
Yaw
Roll
Accel
Gyro
FRONT
TOP
RIGHT

## Slide 8
Internal Measurement Unit (IMU)
Accelerometer
Gyroscope

## Slide 9
Using IMU Data
What benefits are there to having linear acceleration?
What benefits are there to having angular velocity?
What concerns do you have about using the IMU data?
Group activity

## Slide 10
Intel RealSense D435i

## Slide 11
Acceleration
Has three values (in meters/sec2):
  Linear acceleration on X-axis, which points to the right
  Linear acceleration on Y-axis, which points down
  Linear acceleration on Z-axis, which points forward
FRONT of RACECAR

## Slide 12
Gyro
Has three values (in radians/sec) :
  Angular velocity about X-axis (denoted by )
  Angular velocity about Y-axis (denoted by )
  Angular velocity about Z-axis (denoted by )
FRONT of RACECAR

## Slide 13: Physics Module
Retrieves IMU data
Public Interface
  get_linear_acceleration()
  get_angular_velocity()
Notes: https://mitll-racecar.readthedocs.io/en/latest/controller.html

## Slide 14: Examples
Group activity
# Example 1
def update():
accel = rc.physics.get_linear_acceleration()
ang_vel = rc.physics.get_angular_velocity()
if accel[3] > 0.10:
print("Kachow!")
if ang_vel[0] > 0.25:
rc.drive.stop()

## Slide 15: Examples
Group activity
# Example 2
foo = 0
def update():
global foo
ang_vel = rc.physics.get_angular_velocity()
foo += ang_vel[1]
if foo < math.pi / 2:
rc.drive.set_speed_angle(1, 1)
else:
rc.drive.set_speed_angle(1, 0)