## Slide 1: Lab 1
Driving and Controller
This lecture is part of the RACECAR-MN introductory robotics course. You can visit the course webpage at mitll-racecar-mn.readthedocs.io.

## Slide 2: Objectives
Main Objective: Program the car to respond to controller input and drive in predefined shapes
Learning Objectives
Use the start-update paradigm to create a program which can run on the car
Use the drive module to move the car
Use the controller module to respond to input from the Xbox controller in real time

## Slide 3: About the RACECAR-MN

## Slide 4: About the RACECAR-MN
Python
Program
Environment

## Slide 5: About the RACECAR-MN
Python
Program
Inputs
Controller
Color image
Depth image
LIDAR
IMU
Environment

## Slide 6: About the RACECAR-MN
Python
Program
Outputs
Wheel speed
Wheel angle
Inputs
Controller
Color image
Depth image
LIDAR
IMU
Environment

## Slide 7: Car Modes – Default Drive
When you launch a RACECAR program, the car starts in default drive mode so you can easily drive around
Accelerate forward
Accelerate backward
Start user program
Steer
Print message

## Slide 8: Car Modes – User Program
In user program mode, the car is controlled by a Python script using the start-update paradigm
  Start: Run once when the program begins
  Update: Run 60 times per second
Button |  | Effect
Start |  | Enter user program mode
Back |  | Enter default drive mode
Start + Back |  | Exit the program

## Slide 9: Start-Update Paradigm
Example: Demo.py

## Slide 10: racecar_core Library
Exposes easy access to the car's hardware
Under the hood: ROS
Documentation
Implementation
Main
Drive
Physics
Camera
LIDAR
Controller
Display

## Slide 11: racecar_utils Library
Helper functions to process inputs/outputs of racecar_core
You will write everything in racecar_utils during the Jupyter notebook activates throughout the course
Documentation
Implementation

## Slide 12: Drive Module
Controls the car's speed and wheel angle
Public Interface
  set_speed_angle(speed, angle)
  stop()
  set_max_speed(max_speed)
Notes: https://mitll-racecar.readthedocs.io/en/latest/drive.html

## Slide 13: Drive Module - Example
def update():
global counter
if counter < 1:
rc.drive.set_speed_angle(1, 0)
elif counter < 2:
rc.drive.set_speed_angle(1, -0.5)
else:
rc.drive.stop()
counter += rc.get_delta_time()

## Slide 14: Controller Module
Measures input from the Xbox controller
Public Interface
  Button, Joystick, and Trigger enums
  is_down(button)
  was_pressed(button)
  was_released(button)
  get_trigger(trigger)
  get_joystick(joystick)
Notes: https://mitll-racecar.readthedocs.io/en/latest/controller.html

## Slide 15: Controller Module - Example
def update():
if rc.controller.is_down(rc.controller.Button.RB):
speed = rc.controller.get_trigger(rc.controller.Trigger.RIGHT)
rc.drive.set_speed_angle(speed, 0)
if rc.controller.was_pressed(rc.controller.Button.B):
print("Kachow!")

## Slide 16: Lab 1 – Driving in Shapes
Objectives
  Implement default-drive style controls
  A button = drive in a circle
  B button = drive in a square
  X button = drive in a figure eight
  Y button = drive in a shape of your choice
lab1.py