## Slide 1: Lab 2B
State Machines
This lecture is part of the RACECAR-MN introductory robotics course. You can visit the course webpage at mitll-racecar-mn.readthedocs.io.

## Slide 2: Objectives
Main Objective: Write a fully autonomous racecar program to find and park near a cone
Learning Objectives
Design and implement a state machine
Use contour area to estimate object distance

## Slide 3: State Machines
Objective: explore an environment to find a cone
Search

## Slide 4: State Machines
Objective: explore an environment to find a cone
Search
Obstacle

## Slide 5: State Machines
Objective: explore an environment to find a cone
Search
Obstacle
Approach

## Slide 6: State Machines
Objective: explore an environment to find a cone
Search
Obstacle
Approach
Stop

## Slide 7: State Machines
Objective: explore an environment to find a cone
Search
Wander randomly
Obstacle
Turn to avoid obstacle
Approach
Drive toward cone
Stop
Stop moving

## Slide 8: State Machines
Objective: explore an environment to find a cone
Search
Wander randomly
Obstacle
Turn to avoid obstacle
Approach
Drive toward cone
Obstacle out of sight
About to hit something
Stop
Stop moving

## Slide 9: State Machines
Objective: explore an environment to find a cone
Search
Wander randomly
Obstacle
Turn to avoid obstacle
Approach
Drive toward cone
Obstacle out of sight
About to hit something
Stop
Stop moving
Detect cone
Lost the cone

## Slide 10: State Machines
Objective: explore an environment to find a cone
Search
Wander randomly
Obstacle
Turn to avoid obstacle
Approach
Drive toward cone
Obstacle out of sight
About to hit something
Stop
Stop moving
Correct distance from cone
Detect cone
Lost the cone

## Slide 11: Implementation with Enums
from enum import IntEnum
class State(IntEnum):
search = 0
obstacle = 1
approach = 2
stop = 3
cur_state: State = State.search

## Slide 12: Implementation with Enums
from enum import IntEnum
class State(IntEnum):
search = 0
obstacle = 1
approach = 2
stop = 3
cur_state: State = State.search
def start():
"""
This function is run once every time the start button is pressed
"""
global cur_state
cur_state = State.search

## Slide 13: Implementation with Enums
def update():
"""
After start() is run, this function is run every
frame until the back button is pressed
"""
global cur_state
speed: float = 0
angle: float = 0
if cur_state == State.search:
# Set speed and angle to "wander"
if cone_identified:
cur_state = State.approach
if about_to_hit_something:
cur_state = State.obstacle
State behavior
State transitions
(arrows out of state)

## Slide 14: Implementation with Enums
elif cur_state == State.obstacle:
# Set speed and angle to avoid obstacle
if obstacle_avoided:
cur_state = State.search
elif cur_state == State.approach:
# Set angle to face cone and approach
if next_to_cone:
cur_state = State.stop
if not cone_identified:
cur_state = State.search
elif cur_state == State.stop:
speed = 0
angle = 0
rc.drive.set_speed_angle(speed, angle)

## Slide 15: Improvement
Search
Wander randomly
Obstacle
Turn to avoid obstacle
Approach
Drive toward cone
Obstacle out of sight
About to hit something
Stop
Stop moving
Correct distance from cone
Detect cone
Lost the cone

## Slide 16: Improvement
Straight
Drive straight for a while
Obstacle
Turn to avoid obstacle
Approach
Drive toward cone
Obstacle out of sight
About to hit something
Stop
Stop moving
Correct distance from cone
Detect cone
Lost the cone
Turn
Turn to the left
Timer expired
90º turn registered

## Slide 17: Design Strategy
Brainstorm the necessary states
Determine the action in each state
Determine when to transition between states
Iterate: add states/tune relationships as needed

## Slide 18: Implementation Strategy
Create State enum and global variable cur_state
Initialize enum to starting state in start
In update, do the following for each state:
  Create an if block
  Set car outputs (speed, angle, etc.)
  Check for state transitions out of that state

## Slide 19: Exercise
Design a state machine for a "rideshare" program:
  Wanders until receiving a ride request
  Drives to requester, then to their location
Bonus objectives
  How to handle stop signs and stop lights
  How to pass another car
If you have extra time, start converting your state machine into Python (you can use lots of pseudo-code)
Group activity

## Slide 20: Lab 2 – Cone Parking
Objective: Identify an orange cone, align the car with the cone, and park 30 cm away
  Consider what to do if the cone is far from the center and very close to the car
  Stretch goal: how to handle if the cone is out of sight to start?
lab2b.py